## Slide 1: UNIT V MODERN SURVEYING

## Slide 2: Total station surveying
Total station surveying - defined as the use of electronic survey equipment used to perform horizontal and vertical measurements in reference to a grid system (e.g. UTM, mine grid).

## Slide 3: Total Station:
A Total Station is a modern surveying instrument that integrates an electronic theodolite with an electronic distance meter. Total Stations use electronic transit theodolites in conjunction with a distance meter to read any slope distance from the instrument to any particular spot. They are hence two essential surveying instruments in one and when used with other technology such as mapping software are able to deliver the 'total' surveying package, from measuring to mapping.

## Slide 4
Total station is a combination of :
EDM
Theodolite
Auto Leveler
Microprocessor with specific memory
Battery/spare
which works about 5 working hours
About 100 models were released till now by different firms.

## Slide 5: Field techniques with total station
Point location
Slope reduction
Missing line measurement (MLM)
Resection
Azimuth calculation
Remote distance and elevation measurement
Offset measurements
Layout or setting out operation
Area computation
Tracking
Stakeout

## Slide 6: Types of Total Station Surveying
Slope Staking , Topographic surveys, Construction project layout , Leveling Traverse surveys and adjustments, Building Face Surveys, Resections , Areas, Intersections, Point Projections, Taping from Baseline.

## Slide 7: BASIC PRINCIPLE
Although taping and theodolites are used regularly on site – total stations are also used extensively in surveying, civil engineering and construction because they can measure both distances and angles.
Because the instrument combines both angle and distance measurement in the same unit, it is known as an integrated total station which can measure horizontal and vertical angles as well as slope distances.

## Slide 8
Using the vertical angle, the total station can calculate the horizontal and vertical distance components of the measured slope distance.
As well as basic functions, total stations are able to perform a number of different survey tasks and associated calculations and can store large amounts of data.
As with the electronic theodolite, all the functions of a total station are controlled by its microprocessor, which is accessed thought a keyboard and display.

## Slide 9
To use the total station, it is set over one end of the line to be measured and some reflector is positioned at the other end such that the line of sight between the instrument and the reflector is unobstructed (as seen in the figure below).
-The reflector is a prism attached to a detail pole
-The telescope is aligned and pointed at the prism
-The measuring sequence is initiated and a signal is sent to the reflector and a part of this signal is returned to the total station
-This signal is then analysed to calculate the slope distance together with the horizontal and vertical angles.
-Total stations can also be used without reflectors and the telescope is pointed at the point that needs to be measured
-Some instruments have motorised drivers and can be use automatic target recognition to search and lock into a prism – this is a fully automated process and does not require an operator.
-Some total stations can be controlled from the detail pole, enabling surveys to be conducted by one person

## Slide 10: the advantages of Total Station
Relatively quick collection of information
Multiple surveys can be performed at one set-up location.
Easy to perform distance and horizontal measurements with simultaneous calculation of project coordinates (Northings, Eastings, and Elevations).
Layout of construction site quickly and efficiently.
Digital design data from CAD programs can be uploaded to data collector.
Daily survey information can also be quickly downloaded into CAD which eliminates data manipulation time required using conventional survey techniques.

## Slide 11: the disadvantages of Total Station
Vertical elevation accuracy not as accurate as using conventional survey level and rod technique.
Horizontal coordinates are calculated on a rectangular grid system.
However, the real world should be based on a spheroid and rectangular coordinates must be transformed to geographic coordinates if projects are large scale.
Examples : highways, large buildings, etc.
As with any computer-based application “Garbage in equals
Garbage out”. However, in the case of inaccurate construction surveys “Garbage in equals lawsuits and contractors claims for extras.”

## Slide 12: measuring principle of electro optical system
The general principle involves sending a modulated Electro-magnetic (EM) beam from one transmitter at the master station to a reflector at the remote station and receiving it back at the master station. The instrument measures slope distance between transmitter and receiver by modulating the continuous carrier wave at different frequencies, and then measuring the phase difference at the master station between the outgoing and the incoming signals.

## Slide 13
This establishes the following relationship for a double distance (2D):
Where m is unknown integer number of complete wavelengths contained within double distance, Φ; is the measured phase difference and λ is modulation wavelength, and k is constant. Multiple modulation frequencies are used to evaluatem , the ambiguity .

## Slide 14: the different types of EDM
(i) wavelength used (ii) working range (iii) achievable accuracy

## Slide 15: Classification on the basis of wavelength
Present generation EDMIs use the following types of wavelengths (Schoffield, 2001):
(a) infrared (b) laser (c) microwaves
The first two types of systems are also known as electro-optical whereas the third category is also called the electronic system.

## Slide 16: Electro Optical system
Infrared: Systems employing these frequencies allow use of optical corner reflectors (special type of reflectors to return the signal, explained later) but need optically clear path between two stations. These systems use transmitter at one end of line and a reflecting prism or target at the other end.

## Slide 17
Laser: These systems also use transmitter at one end of line and may or may not use a reflecting prism or target at the other end. However, the reflectorless laser instruments are used for short distances (100 m to 350 m). These use light reflected off the feature to be measured (say a wall).

## Slide 18: The working principle of Electro-optical system or EDM
An EDM uses electromagnetic (EM) energy to determine the length of a line. The energy originates at an instrument at one end of a line and is transmitted to a "reflector" at the other end from where it is returned to the originating instrument.

## Slide 19: The working principle of Electro-optical system or EDM
The nature of the "reflector" is dependant on the type of EM. If electro-optical (infrared or laser) EM is used then the "reflector" is typically a passive medium which bounces the signal back. If the EM is microwave, then the reflector is a second instrument which captures the incoming energy and re-transits it back to the originating instrument.

## Slide 20
Thank You